Disc Sander

Safety Exam

Points earned ______/15				Name _____________________________

Directions:  You are to write the letter U in the space to the left of the statement if you believe the statement to be unsafe.  You are to write the letter S if you believe the statement to be safe.

1. _____ To wear safety glasses.

2. _____ To roll up all sleeves and tuck in loose clothing.

3. _____ To use gloves when sanding.

4. _____ To talk to or distract someone using the disc sander.

5. _____ To use a disc that is worn out.

6. _____ To sand at the 9 o'clock position.

7. _____ To move the work piece periodically to keep the disc from burning/scorching.

8. _____ To use more force as the disc becomes worn.

9. _____ To place your fingers near the sanding surface.

10. _____ To remove large amounts from work pieces on the disc sander.

11. _____ To put your work piece against the disc and then turn it on.

12. _____ To periodically clean the disc with rubber disc cleaner.

13. _____ To always have the dust collector on.

14. _____ To sand steel or make sparks on the disc sander.

15. _____ To make any adjustments with the machine off.

f:disc sander safety quiz