Wood Science

Page 1

Tree-A plant growing at least 20 feet tall and supported by

a single stem

- NATURE OF WOOD

  - Hard and Softwoods

    - Hardwoods (deciduous)

      - Trees that shed their lives

      - Trees that have broad leaves

      - Bear a fruit or nut

      - Oak, Walnut, Maple are examples

    - Softwoods (coniferous)

      - Cone bearing trees

      - Needle like leaves

      - Do not lose their leaves (needles)

      - Pine, Cedar, Fir are examples

  - Open vs. Closed Grain Wood

    - Open grain wood

      - Open pores

      - Accept stain well

      - Oak, Walnut, Ash are examples

    - Closed Grain Woods

      - Pores are closed

      - Do not accept stain well

      - Fir, Pine, Cedar, Maple are examples

Wood Science

Page 2

  - Structure of wood

    - Cellulose-strands that line cells and wrap the cells together

    - Lignin-“glue” that hold cells together

  - How a tree grows

    - Springwood grows quicker due to increased moisture

    - Summerwood is darker and grows slower

    - Annual growth rings show both summer and springwood.

  - Parts of a tree

    - Pith is the porous center

    - Heartwood is the mature wood around the pith

    - Sapwood is the newer recent growth and is lighter in color than heartwood.

    - Cambium layer is the area where cell formation takes place.

    - Inner bark carries food and nutrients to the cambium layer

    - Outer bark is a dead corky substance that protects the trees inner layers.

  - Moisture Content

    - All wood is dried in the open air or a kiln

    - Lumber for homes is dried to 19% or less

    - Lumber for furniture is dried to 6-10%

Wood Science

Page 3

- Properties of Wood

  - Specific Gravity

    - Ratio of a piece of wood to its same weight in water.

    - Most wood floats because its specific gravity is less than that of water.

    - Woods with a specific gravity more than one will sink (Leadwood from Africa)

  - Wood Porosity

    - Open spaces in wood

    - How well liquid will transfer through wood

    - Red Oak and Whiskey barrels

  - Other Properties in Wood

    - Bending strengths

    - Insulating property

    - Shock absorption

  - Trees and Pollution

    - For every 2000 pounds of wood in a tree, 2900 pounds of carbon dioxide is consumed and 2100 pounds of oxygen is released.

    - Wind break slow dust particles in the air and allow them to settle out.

    - Sulfur dioxide, ozone, ethylene are pollutants that kill trees.

Wood Science

Page 4

  - Trees and pollution cont.

4. Trees hold soil and slow water erosion.

5. Trees planted properly in urban settings can reduce

noise by 50%

  - Wood and Energy

    - Wood is the only renewable raw material.

    - Trees consume solar energy.

    - Conversion of trees to lumber requires little energy.

    - Wood is biodegradable.

  - Wood as an Insulating Material

    - 6 times better than brick

    - 15 times better than concrete

    - 1,770 times better than aluminum

f:wood science notes